# Input Section

| Impedance | 10kOhm, Electronically Balanced |
| --- | --- |
| Max. Input Level | +20dBu |
| Connector | XLR331 or equivalent |

Output Section

| Output | Electronically Balanced & floating |
| --- | --- |
| Max. Output Level | +20dBu into 600 Ohms |
| Connector | XLR332 or equivalent |

System Performance

| Frequency Response | +/0.25dB 20Hz to 20kHz |
| --- | --- |
| Distortion (THD) | <0.005% 20Hz to 20kHz @+4dBu |
| Output Noise (flat) | <90dBu, 22Hz to 22kHz, unweighted |
| Channel Separation | Better than 80dB from 20Hz to 20kHz |
| Gain Control Range | +/10dB |
| Peak Indicator | +18dBu |
| Bypass | Passive failsafe bypass relay |

Filters

| Type | MFB Constant Q |
| --- | --- |
| Frequencies Per Channel | 30 off, on 1/3 octave ISO centres, 25Hz to 20kHz |
| Boost/Cut Range | Nominal +/10dB * |
| Mode | Selectable normal or fine response |
| High Pass Filter | 18dB/octave Butterworth, 20Hz to 250Hz |

General

| Power Requirements | AC 30VA 50/60Hz, selectable 90/120v or 190/250v. IEC AC power cord. |
| --- | --- |
| Dimensions | 3U 19 " x 5.25" x 8.9" (482mmx132mmx227mm) |
| Weight | 11lbs gross shipping (6kg) |

Options

|  | Transformer Balancing (Input and Output) |
| --- | --- |
|  | Security Cover (2U, 3U) |